Figure: MAPT Manifold Air Pressure and Temperature sensor for Hyundai (H100, H-1, etc.) and KIA, but I will use it for something else.

OEM #: 3920042030
EAN: 4059191686698

Pressure sensor core type: Piezoelectric capacitance (?)
Origin: AliExpress, no brand, China generic

The pins are numbered on the top of the housing (but not visible in these pictures),
from right to left in the right picture:
1. GND, for power and signal reference
2. MAT output: NTC
   Measured: 2.2 kΩ to pin #1 at 20 °C
   Measured: approx. 330 Ohm to pin #1 at approx. 95 °C.
   Measured values fit with NTC Beta = 2800
   (measured: 7.08 kΩ to pin #3 at 20 °C, with 0 mV at pin #3)
   Measured: 0.0 mV to pin #1 with 5000 mV at pin #3.
3. 5 V power input
   Current: TBD
   Can it be used at 3.3 V power input? (That would interface easier with a STM32.)
4. MAP output, analog, linear, 11 – 254 kPa absolute = 250 – 4759 mV
   Measured: 1849 mV at 97 kPa and 5000 mV power input,
   vs. theoretical: 250 + (97-11)/(254-11) * (4759-250) = 1846 mV.

   Measured: 1213 mV at 97 kPa and 3300 mV power input,
   vs theoretical 1846 mV * 3300/5000 = 1218 mV.
   The output seems to be proportional to the input voltage.

Electronics HW and SW for MAP-sensor – work in progress (not complete)

HW and tools used: WeActStudio's STM32WB55CoreBoard and STMLinkV3MiniE, and Windows PC with STM32CubeMX, STM32CubeIDE, STM32CubeProgrammer.
A phone with Android and the apps “LightBlue” and “ST BLE Toolbox” and Racechrono-Pro.

The STM32W MCUs have two cores. Core #2 is a ARM Cortex M0 linked to the radio HW. It runs ST's proprietary FW, e.g. one with a full and certified BLE interface, or a smaller FW with a limited BLE (there are also firmwares for other radio protocols). Connect the HW and use the STM32CubeProgrammer to check (and maybe also update) the bootloader and flash the FW needed for our project! Follow the instructions in the FW release notes!

Connect the debugger to both the CoreBoard’s SW-debug and to USART1 TX/RX. The FW in debug-mode writes messages via USART1. Check Windows device manager and open a serial terminal to to the CoreBoard via the debugger. CubeIDE has an integrated terminal, select; -- ViewMoreConnectionsNew connection….

Watch ST’s STM32WB video tutorials, in particular this: https://youtu.be/Zgw3wRpGSRQ?t=195
Watch Phil's Lab #129 on YouTube.
See https://github.com/aollin/racechrono-ble-diy-device

STM32CubeMX:
Hover the mouse/pointer over Middleware STM32_WPAN to check pre-requisites
System Core  HSEM (hardware semaphores)  Activate
System Core  IPCC Activate
System Core  IPCC NVIC Settings  IPCC RX and TX interrupt
Timers  RTC  Activate Clock Source, and also select
Timers  RTC  WakeUp: Internal WakeUp
Timers  RTC  NVIC  Enable RTC wake-up …
Connectivity  RF  Activate RF1
STM32_WPAN → Application and services → Select “Custom Template”
(Do not enable FREERTOS, it is not compatible with WPAN/BLE Custom template)
STM32_WPAN → BLE Advertising → Advertising Elements → AD_TYPE_COMPLETE_LOCAL_NAME Yes
STM32_WPAN → BLE Advertising → Advertising Elements → AD_TYPE_COMPLETE_LOCAL_NAME = NinoDAQ
STM32_WPAN → BLE GATT → Number of services = 1
STM32_WPAN → BLE GATT → Long Name = RaceChrono_BLE_DIY
STM32_WPAN → RaceChrono_BLE_DIY → Number of characteristics = 2
STM32_WPAN → RaceChrono_BLE_DIY → Service 1 → UUID = 00 00 1F F8 00 00 10 00 80 00 00 80 5F 9B 34 FB
STM32_WPAN → RaceChrono_BLE_DIY → Characteristics 1 → UUID = 00 01
STM32_WPAN → RaceChrono_BLE_DIY → Characteristics 1 properties → CHAR_PROP_READ=Yes, CHAR_PROP_NOTIFY=Yes, other CHAR_PROPs = No
STM32_WPAN → RaceChrono_BLE_DIY → Characteristics 2 → UUID = 00 02

Generate code. In STM32CubeIDE:
Core → Src → main.c → PeriphCommonClock_Config(void) → Add line LL_HSEM_1StepLock(HSEM,5);

STM32_WPAN → App → custom_stm.c → Add #include "usbd_cdc_if.h"

# Compressor Efficiency Estimation

Place one MAPT sensor at the compressor inlet (i.e. after the air filter) and another MAPT at the compressor exit (i.e. before the intercooler). The compressor’s efficiency (relative to an isentropic compression) can then be calculated as:

Temperatures in Kelvin and absolute pressure must be used. However the units are handled automatically when using Mathcad, so the evaluation in Mathcad gives correct result regardless of temperature and pressure unit-combinations, for example like this:

Note that the temperature sensor in the MAPT reacts rather slowly. The calculated efficiency will therefore only be valid at steady conditions (i.e. not while driving in a car, maybe OK for a long uphill, or for a boat).